## Slide 1: UTC – Austin Final Report
Zane White, Morgan Linsey, Kevin Crock, Rodrigo Ramirez, Abigail Chace

## Slide 2: Agenda
Introduction
Data
Methodology
Weighting Matrix
Findings
Challenges
Limitations
Conclusion
Q&A Sessions

## Slide 3: Introduction
Austin has the need for an urban tree canopy vulnerability index
The index allows city officials to visualize and locate areas for tree development and tree loss
Vulnerability index created from environmental constraints and impervious cover data

## Slide 4: Data
Boundaries
Environmental Constraints
Planning Cadastral
Risk Indices
Tree Canopy Vulnerability index
Entity | Spatial Objects | Status | Source
Austin Tree Canopy Data | Cellular Raster | Available | City of Austin
Current Austin Zoning | Polygon | Available | City of Austin
Proposed Austin Zoning | Polygon | Available | City of Austin
Austin City Limits Boundary | Polygon | Available | City of Austin
Creek Buffers | Polygon | Available | City of Austin
Critical water quality zones | Polygon | Available | City of Austin
Edwards Aquifer Zone | Polygon | Available | City of Austin
Floodplains | Polygon | Available | City of Austin
Erosion hazard zone | Polygon | Available | City of Austin
Wetlands | Polygon | Available | City of Austin
Social Vulnerability Index | Polygon | Available | City of Austin
Community Wildfire Risk | Polygon | Available | City of Austin
Climate Vulnerability Index | Polygon | Available | City of Austin
Zoning Proposed | Polygon | Available | City of Austin
Transit priority network and LA corridors centers | Polygon | Available | City of Austin
Impervious Cover 2017 | Polygon | Available | City of Austin
Steep Slopes | Polygon | Available | City of Austin

## Slide 5: Methodology
Clipped all data
Necessary Raster-to-Vector Conversion
Intersect all data
Calculated Percentages of Intersection for all environmental constraints

## Slide 6: Methodology
Source: ResourcesEsri.com
Merged Duplicates
Data Repair
Spatial Join all files to Zoning File / Boolean Calculation
Multiple weights to percentages
Summarize weighted fields = VI
More

## Slide 7: Weighting Matrix
Variables were weighted from a -5 to 5 scale based on literature review
Values were multiplied by percent coverage of each variable per parcel
Addition of sums used to create index
Variables | Weighted Value
Impervious Cover | -5
Transit Priority Network | -5
Rock Outcrops | -5
Critical Water Quality Zones | -4
Erosion Hazzard Zones | -4
Steep Slopes | -3
Seeps and Springs | 2
Edwards Aquifer Zones | 2
Creek Buffers | 4
Floodplains | 4
Wetlands | 5
Tree Canopy | 5

## Slide 8: Findings
Standard Deviation
Bimodal
Very Little Skew
Regression Analysis
Relationship between Tree canopy Index and Impervious cover
R2 = .31

## Slide 9: Implications
Zoning R2A and R2C
  Residential with 2 units
Transit Priority Network
Centered around IH-35
Commercial Development

## Slide 10: Challenges
Godzilla Dataset
  Tree Canopy File Over 1 Million Rows & Over 2 Million Polygons
Processing Power
  Switching To Personal Computers
  Crashes, Errors, Incorrect Outputs
  Calculations
Data Management & Sharing
  Layer Files
  Joined Fields
  Passing Of Large Dataset Files
https://ak0.picdn.net/shutterstock/videos/7675090/thumb/5.jpg

## Slide 11: Limitations
Data Inconsistency
  Tree Canopy File 2014
Soil Data
  Remote Sensing Data
  Rich Soils Vs. Poor Soil
Additional Data
  Air Pollutants
  Land Cover Types
  Rainfall
https://kofirm.com/wp-content/uploads/2019/06/iStock-1094790212-Cropped-e1560895210306.jpg

## Slide 12: Conclusion
Developed the Tree Canopy VI
Located where tree canopy is vulnerable to decline regarding current and proposed zoning policies
Made a Tree Canopy VI Webmap for the Public

## Slide 13
Q&A Session
?

## Slide 14: References
Armson, D., et al. “The Effect of Street Trees and Amenity Grass on Urban Surface Water Runoff in Manchester, UK.” Urban Forestry & Urban Greening, Urban & Fischer, 17 May 2013, www.sciencedirect.com/science/article/pii/S1618866713000460.
Greene, Christopher S., and Peter J. Kedron. “Beyond Fractional Coverage: A Multilevel Approach to Analyzing the Impact of Urban Tree Canopy Structure on Surface Urban Heat Islands.” Applied Geography, Pergamon, 19 Apr. 2018, www.sciencedirect.com/science/article/pii/S0143622817301935.
Hill, Elizabeth, et al. “Evaluating the Impact of Government Land Use Policies on Tree Canopy Coverage.” Land Use Policy, Pergamon, 2 July 2009, www.sciencedirect.com/science/article/pii/S0264837709000647.
Halter, Alan Dale. “Determining Existing, Possible, and Preferable Urban Tree Canopy for Austin, Texas.” TexasScholarWorks, University of Texas at Austin, 1 May 2013, hdl.handle.net/2152/22682.
Weissmann, Jordan. “Austin, Texas, Is Blowing Away Every Other Big City in Population Growth.” Slate Magazine, Slate, 21 May 2015, slate.com/business/2015/05/population-growth-in-u-s-cities-austin-is-blowing-away-the-competition.html.
“Urban Population Growth.” World Health Organization, World Health Organization, 16 Mar. 2015, www.who.int/gho/urban_health/situation_trends/urban_population_growth_text/en/.